DL Factory Technical Meeting
(Kick-Off)
Team :
Alan Muir
Philip Heath
Mike Lowe
Dan Salisbury
Dave Sim
Sotiris Vlachos
Carlos Chavez
Ged Bell
Anyssa Navrer-Agasson

---
Agenda
Personnel safety
Machine Protection
Tension Control System
Winding Head
Latching Mechanism
Tension Measurements (Laser & DWA)
Calibration system for Layer winding (recipe automation and camera)

---
Safety
- Personnel safety
  - Much improved from the original design, light curtain, SLS (safety limited speed) etc.
  - Need to consider what else is needed following safety review.
- Machine Protection
  - much improved from original. Jog controls disabled, safe zones introduced, command line filtering and protection.

---
Controls
- Tension Control System
  - Has to be in spec for the success of the project.
  - The better the machine performs - less time spent manually re-tensioning.
  - Need to test wires straight after they are wound to see how the machines are performing - is good tension being lost after moving the APA?
  - Consider moving the load cell amplifier to the winding head
- Latching Mechanism (does it need improvements?)
- Winding Head
  - Scheduled maintenance - TPM and PM
  - Improvements? Pulley and roller materials. Spring housing materials. Better machined sprockets.
  - Alternative lubricants - particularly for the spring housing, grease vs oil.

---
Measurements & Winding recipes
- Tension Measurements (Laser & DWA)
  - DWA developments, schedule
  - Aiming to reduce the use of Laser system in the future
- Calibration system for Layer winding
  - recipe automation
  - Camera and PLC integration