## Slide 1: Liquid Argon R&D ARIADNE+ results and future testing on ProtoDUNE
Adam Roberts
(on behalf of the ARIADNE+ collaboration)
+
http://hep.ph.liv.ac.uk/ariadne

## Slide 2: ARIADNE Detection Principle
ARIADNE has demonstrated light readout as a viable alternative to charge in dual-phase TPC neutrino experiments
Incoming particles ionise LAr and create prompt scintillation light (S1)
Electrons drift towards the extraction grid situated below the liquid level
A THGEM (THick-Gaseous Electron Multiplier) amplifies drift charge (capable of >30 kV/cm in LAr) generating secondary scintillation light (S2)
WLS (Wavelength Shifting) before imaging with Timepix3 camera
ARIADNE (ARgon ImAging DetectioN chambEr)
Cameras

## Slide 3: The ARIADNE Advantage - Optical TPCs
    High Resolution: For e.g. TPX3 camera has 256 x 256 pixels, imaging 35 x 35 cm area, as on ARIADNE, gives ≈ 1 mm resolution
    Sensitivity to low energies: Gain is generated by the THGEM; a THGEM accelerated electron can generate upwards of 100 photons, cameras can be sensitive to single photons
    Low Noise: Externally mounted cameras are decoupled from TPC electronic noise sources/acoustics
    Ease of Access: Cameras can be accessed while TPC is operating
    Cost Efficient: No need for thousands of internal charge TPC readout channels, pre-amps etc.
    Available now
ARIADNE 1-ton detector
Dual phase TPCs enable low energy physics and are the established technology for direct dark matter detection
  Benefits:
TDR: https://iopscience.iop.org/article/10.1088/1748-0221/15/03/P03003

## Slide 4
Larger Scale Demonstration at the CERN Neutrino Platform
CERN LOI: https://cds.cern.ch/record/2739360
Test optical readout on a scale relevant for DUNE using the existing CERN cold box
Recent Operation March/April 2022

## Slide 5: ARIADNE+: Cryostat Optical Configuration
TPX3 Camera (1 x VUV)
Light Readout Plane (LRP)
Cathode
TPX3 Cameras (3 x visible)
Large scale test of ARIADNE optical readout principle for dual-phase LArTPCs.
Four Timepix3 based cameras, each covering 1m x 1m readout area.
Three cameras detect visible light (wavelength shifter installed above THGEMs)
One camera directly images VUV.

## Slide 6: TPX3 Camera System
Timepix 3 Camera
Relay optics
Image intensifier
Objective lens

## Slide 7: Re-entrance Viewport
Visible lenses (f0.95, 10.5 mm)
Custom made VUV MgF2 Lens (f3, 11mm, 5mm diameter)

## Slide 8: Light Readout Plane (LRP) Design
Bottom view
Photochemically etched extraction grids
THGEMs/Extraction grids supported by PEEK Spacers
2.3m
50cm x 50cm G-THGEMs
Welded Invar structure (Uniquely low coefficient of thermal contraction)
Modular design which can be applied directly to a DUNE module

## Slide 9: Glass THGEMs
Sixteen 50cm x 50cm glass THGEMs
1.1mm thick,
500μm ID holes,
800μm pitch hexagonal array
Novel Glass THGEMs developed at Liverpool (Patent accepted GB2019563.2)
See for more details:
https://www.mdpi.com/2076-3417/11/20/9450

## Slide 10: Light Readout Plane (LRP)
LRP assembly at CERN

## Slide 11: Cold box Integration

## Slide 12: Cold box Integration

## Slide 13: Closing the Detector

## Slide 14
Closing the Detector

## Slide 15: Detector running
Very stable cryogenic operation thanks to the CERN team
Argon purity was approximately 0.5 msec
Three weeks of data collection refilled twice

## Slide 16: 30 Seconds Integral Cosmics
Visible cosmics
VUV cosmics
(Additional vignetting from VUV optics)

## Slide 17: Sample events

## Slide 18: ARIADNE+ Conclusions
Optical readout achieved with stable detector conditions has been demonstrated at the same scales as that for vertical drift tests (CERN Neutrino Platform Cold Box)
Dual phase extraction region very stable at large scale!
TPX3 and Glass THGEM technology is ready for deployment now
An option for DUNE LAr Far Detector, DUNE LAr Near Detector and DUNE GAr Near Detector (if enough light is produced in pressurised gas Argon. Tests are in preparation in collaboration with USC –Diego’s group)
ProtoDUNE is the natural platform to perform the next essential steps

## Slide 19: Using ProtoDUNE dual phase to test optical readout for Neutrinos and DM

## Slide 20
Eight TPX cameras (1mx1m) using the current cryostat ports (green shaded areas)
Dedicated readout area for other optical sensors (e.g. Darkside SiPMs) for very low energy thresholds
X-Arapucas integrated into the field cage to test light detection technologies for future DUNE modules.
16 Darkside-20k PDUs produced in the UK
TOP VIEW Optical protoDUNE
X-ARAPUCAs
TPX3 Cameras

## Slide 21
Eight TPX cameras (1mx1m) using the current cryostat ports (green shaded areas)
Dedicated readout area for other optical sensors (e.g. Darkside SiPMs) for very low energy thresholds
X-Arapucas integrated into the field cage to test light detection technologies for future DUNE modules.
16 Darkside-20k PDUs produced in the UK
TOP VIEW Optical protoDUNE
X-ARAPUCAs
TPX3 Cameras

## Slide 22: Darkside SiPMs

## Slide 23: Darkside SiPMs
We plan to soon (before the end of the year) run ARIADNE to test the proposed instrumentation for protoDUNE.
Three cameras will be installed, with the remaining ¼ of the detector dedicated to Darkside SiPMs.
Measure the response of Darkside SiPMs to varying THGEM bias and determine the correct gain for protoDUNE operation.
Study sensitivity/threshold/resolution differences between Darkside SiPMs and Timepix cameras and asses possible new physics which can be accessed in view of DUNE.

## Slide 24: Timeline
Testing of Darkside SiPMs in ARIADNE
Design of LRPs for protoDUNE
Today
2024
2025
2026
Formation of protoDune working group (Arapuca, Darkside)
Submit proposal to SPSC
Proposed installation on protoDUNE
Facility at Liverpool for GTHGEM production

## Slide 25: GTHGEM production facility
Guyson Euroblast 9 enclosure which we will fit
with custom mechanics/controls for automated machining process

## Slide 26
Thank you