## Slide 1: Atom Interferometry: MAGIS & AION @ Liverpool Progress

## Slide 2: University of Liverpool Team
Sam Hindley

## Slide 3: Atom Interferometry at University of Liverpool
AION
MAGIS
Liverpool
(poster of Leonie Hawkins)

## Slide 4: Atom Interferometry at Liverpool
~1m experiment
Old system is being de-commissioned
Two new chambers acquired
  One from NPL
  One being built in-house
Upgraded the laser system
  Allows atom launch
  Increased power and frequency control of interferometry beams
2D and 3D MOTs recently achieved!
  See Leonie Hawkins poster
NPL chamber in Liverpool
New chamber being assembled in Daresbury

## Slide 5: MAGIS-100: DM & GW detector prototype at Fermilab
100-meter baseline atom interferometry in existing shaft at Fermilab
The construction at Fermilab delayed to 2025
  10m prototype under construction in Stanford University
  Finalising & prototyping the 100m designs
3 atom sources to realize a gradiometer
Intermediate step to full-scale (km) detector for gravitational waves
Probes for ultralight scalar dark matter beyond current limits
Matter wave Atomic Gradiometer Interferometric Sensor
https://iopscience.iop.org/article/10.1088/2058-9565/abf719
Notes: MAGIS = Matter wave Atomic Gradiometer Interferometric Sensor
Add photo of area….
John Hopkins Logo, STFC, DOE, Kavli

## Slide 6
Stanford Prototype MAGIS-10
https://hoganlab.stanford.edu/research/strontium-gradiometer

## Slide 7: Atom Interferometry & Gradiometry
Two identical atom interferometers are run simultaneously using the same laser sources
Signals is a differential measurement
Enables the cancellation of noise common to both interferometers
Measured phase difference is proportional to the gradient of the local gravitational force
Notes: Signals is a differential measurement that enables the cancellation of noise common to both interferometers

## Slide 8: Searches for Light Dark Matter
The ultra-light dark matter acts as a classical field
Many detection techniques, e.g. atom interferometers
DM coupling causes time-varying atomic energy levels:
DM induced oscillation
Time
Dark matter coupling

## Slide 9: Projected Sensitivity to Dark Matter
Sensitivity to ultralight scalar dark matter coupled via electron mass a) and fine structure constant b) [Mahiro Abe et al 2021 Quantum Sci. Technol. 6 044003, 2021]
  1 year of data taking in scalar DM configuration
  Assuming atom shot-noise limited phase resolution
  Gravity gradient noise (GGN) not included – mass density fluctuations
  The updated sensitivity curves including GGN
  Phys. Rev. D 107, 055002, 2023
Notes: The projected reach of these experiments is ultimately limited by fundamental noise sources. Vertical gradiometers such as AION and MAGIS-100 are designed to reach the atom shot-noise limit above ∼1 Hz but would suffer from gravity gradient noise (GGN) at lower frequencies. This type of phase noise arises as a result of mass density fluctuations of the ground and atmosphere, which perturb the local gravitational potential around the atom clouds. In the absence of a well-modeled GGN signal for vertical atom interferometers, previous projections were either abruptly interrupted at ∼0.3 Hz , or arbitrarily extended to lower frequencies by assuming atom shot noise only . [https://journals.aps.org/prd/pdf/10.1103/PhysRevD.107.055002]

## Slide 10: Liverpool deliverables in AION & MAGIS
Design & manufacturing:
In-vacuum optics mounts – almost finished
  Big thanks to Liverpool Detector Development Manufacturing Facility & K. Bridges
Top tip-tilt platform – in queue
Phase shear detection system – manufacturing
  Retro-reflection chamber & its control
  Two control loops are being developed, see H. Throssell & K. Hussain talks
Sourcing in-vacuum interferometry optics
  Ordered & being manufactured at Optimax

## Slide 11: Atom Interferometer Observatory & Network
5 new Sr labs established
  5x atom sources/interferometers
  Commissioning phase
AION-10 planned construction at Beecroft building, Oxford
  Preliminary design review passed
Location of AION-100 Boulby
  Network with MAGIS for improved sensitivity to DM & GWs
3D MOT @ Birmingham
3D MOT @ Imperial
Notes: 100m baseline – MINOS access shaft – LARGE NOT LARGEST
Sensitivity proportional to interrogation time
3 interferometers, 3 Sr atom sources
  Differential measurements
Networking with AION in UK

## Slide 12: AION Days at Liverpool
Liverpool hosted AION Days in November 2022
2 day event
50 collaborators attended in person
Talks given by core MAGIS team as well

## Slide 13: Summary - Deliverables
Retro-reflection phase-shear platform manufacturing is ongoing
  PZT cabling design approved
  UHV testing done
  Prototyping PZT control in-progress
Manufacturing of parts is expected on schedule
  Lattice launch mounts shipped (98%)
  Most parts of retro-chamber finished (80%)
The design of Top Tip-Tilt platform is completed
  Equipment has been specified, ordered & shipped
  Manufacturing starting soon of mirror mount and chamber starts in summer
Sourcing in-vacuum interferometry optics completed

## Slide 14: Summary – Key moments
University of Liverpool hosted AION Days
Kamran Hussain started joint PhD with RAL and Liverpool
  Going to RAL this summer
Sam Hindley submitted first MAGIS-UK thesis
University of Liverpool laboratory acquired an experimental chamber from NPL
  Rb 3D MOT established
New chamber being assembled at Daresbury

## Slide 15: Backup

## Slide 16: AION Sidearms

## Slide 17: Retro-reflection Phase-shear Platform
UHV chamber housing retro-reflection mirror
Mirror needs precise control for
  Phase-shear imaging
  Interferometry beam monitoring and alignment
  Coriolis corrections
  Designed in collaboration with the University of Liverpool, Stanford, Northwestern Universities and Fermilab
  AION plans to use the platform too

## Slide 20: Testbed for GW sensor
Recent discovery of 150 solar mass black hole merger by LIGO is encouraging as heavier mergers would occur in the mid-band frequency range.
Notes: As a technology demonstrator, MAGIS-100 is not expected to be sufficiently sensitive to detect known candidate sources of gravitational waves. Nevertheless, within its frequency range it aims to achieve a record sensitivity, improving on the current bounds.
Additionally, the recent discovery by LIGO of a binary black hole merger with a total mass of 150 solar masses motivates further studies of intermediate mass black holes. Earlier observations of such binaries at lower frequencies (including mid-band frequencies) would provide valuable astrophysical insight. Moreover, even heavier black holes than the LIGO observation, hundreds of solar masses and above, would merge in the mid-band. Therefore, this would be the ideal band to discover such black holes, if they exist.