## Slide 1: Current Intensity limits and possible upgrades in M2
D. Banerjee on behalf of BE-EA-LE
Date: 09.11.2023

## Slide 2: The M2 Beam
Three main operation modes:
  High-energy, high-intensity muon beam. Normally for muon momenta up to 200 GeV/c.
  High-intensity secondary hadron beam for momenta up to 280 GeV/c with radiation protection constraints.
  Low-energy, low-intensity (and low-quality) in-situ electron calibration beam.
Beam Mode | Momentum (GeV/c) | Max. Flux (ppp / 4.8s) | Typical Dp/p (%) | Typical RMS spot at COMPASS target | Polarisation | Absorber (9.9 m Be)
Muons | +208/190 +172/160 | ~108 2 108 | 3.7% | 8 x 8 mm | 80% | IN
Hadrons | +190 -190 Max. 280 | 108 (RP) 4 X 108 (with dedicated dump) | ₋ | 5 x 5 mm | ₋ | OUT
Electrons | -10 to -40 | < 2 10 4 | ₋ | > 10 x 10 mm | ₋ | OUT
D. Banerjee on behalf of BE-EA-LE

## Slide 3: The M2 Beam – Parameters and Principle
T6
EHN2
Hadron
absorber
π,K
µ
Scrapers
BEND 6
p
600 m
400 m
Hadron Decay Section
Muon Cleaning Section
(172 ± 17) GeV/c
(160 ± 6) GeV/c
Beam Parameters as was used for COMPASS | Measured
Beam momentum pµ/pπ | 160 / 172 GeV/c
Proton flux on T6 per SPS cycle | 1.5 1013
Muon flux at COMPASS per SPS cycle | 2 108
Beam polarisation | -80% ± 4%
Spot size at COMPASS target (σx x σy) | 8mm x 8mm
Divergence at COMPASS target (σdx x σdy) | 0.4mrad x 0.8mrad
Muon halo within 50mm from beam axis | 16%
Halo in experiment (6 x 4m2) at ¦x,y¦>150mm | 7%
D. Banerjee on behalf of BE-EA-LE

## Slide 4: Beam Flux
Factor typically factor 2.7 smaller for µ– at same momentum.
At around 110 GeV/c the muon rate can be increased by about 40% compared to 160 GeV/c but currently limited by radiation protection considerations.
Flux for µ+ at 1.3 1013 ppp and for fixed pµ/pπ ratio (polarisation = 0.8)
Muon momentum [GeV/c]
Muon Flux (x 107)
D. Banerjee on behalf of BE-EA-LE

## Slide 5: CERN Prevessin site – EHN2
TLD (some TLDs added since 2015)
EHN2
Downstream of COMPASS (SMS823)
Dose due to muons
Decision to add TLDs at end of site in 2018
Lateral to COMPASS (SMS824)
Dose due to neutrons (skyshine) relevant for hadron beam
2018: Shielding had been increased to mitigate neutron dose, however experimental program also required higher beam intensity than in 2015.
Amongst others, objective was to remain < 1 mSv at the fence (CERN code F)
Stray radiation monitoring stations
C. Ahdida HSE-RP

## Slide 6: SMS823 dose rates during 2022
Nominal beam period
Background period
2022 beam operation
The maximum dose rate registered by SMS823 during COMPASS beam operation in 2022 amounted to a net value of ~1.8 uSv/h
The average dose rate during nominal beam operation amounted to a net value of ~1.4 uSv/h
Dose rate in accessible area upstream and downstream of SMS823 to be below the area classification - limit of 2.5 µSv/h.
C. Ahdida HSE-RP

## Slide 7: Muon beam profiles downstream of EHN2
Downstream exclusion zone
SMS823
HALO simulations performed to study the muon beam distributions downstream of EHN2. Attenuation inside of the soil is neglected
Maximum observed at the beam axes (near the centre)
Up-down asymmetry in the halo particles (as expected) coming from the tunnel, which disperses more downstream at the SMS823 location
At location SMS823 the muon intensity at the ground level is expected to be about a factor 1.3 lower than at the end of the exclusion zone  1.82 µSv/hr
102
102
Beamline
Beamline
Ground level
Ground level
C. Ahdida HSE-RP

## Slide 8: Muon beam profiles downstream of EHN2
Far downstream (close to fence)
Far downstream (close to fence)
HALO simulations performed to study the muon beam distributions downstream of EHN2. Attenuation inside of the soil is neglected
Maximum observed at the beam axes (near the centre)
Up-down asymmetry in the halo particles (as expected) coming from the tunnel, which disperses more downstream at the SMS823 location
At the location SMS823 the muon intensity at the ground level is expected to be about a factor 2 higher than at the far downstream location close to the CERN fence.  0.7 µSv/hr
102
SMS823
102
Beamline
Ground level
Beamline
Ground level
C. Ahdida HSE-RP

## Slide 9: Muon beam profiles downstream of EHN2
HALO simulations performed to study the muon beam distributions downstream of EHN2. Attenuation inside of the soil is neglected
Maximum observed at the beam axes (near the centre)
Up-down asymmetry in the halo particles (as expected) coming from the tunnel, which disperses more downstream at the SMS823 location
At location SMS823 the muon intensity at the ground level is expected to be about a factor ~2.8 lower than at the upstream part of the exclusion zone  3.9 µSv/hr
Beamline
Beamline
Beamline
Beamline
Exclusion zone
SMS823
Ground level
Ground level
102
102
Exclusion zone
Beamline
C. Ahdida HSE-RP

## Slide 10: Increased hadron beam intensity Future AMBER DY run post-LS3

## Slide 11: Increased annual intensity
In order to improve the accumulated kaons for future AMBER Drell-Yan run the hadron beam intensity increase was also studied.
RP studies were performed to check additional shielding for higher intensities to comply with the radiation area classification, calculate prompt radiation, skyshine optimisation and environmental impact.
The source term used included 190 GeV/c π- beam with an instantaneous intensity of 4.8x108 π-/spill and 240 spills/h on the AMBER target.
The aim was to validate the increase of the accumulated annual intensity to 3 x 1014 π-/year on the AMBER target.
A. Devienne, C. Ahdida HSE-RP

## Slide 12: Proposed modifications
Hole to be filled with concrete bricks
concrete bricks
(support and fixation to be studied)
Remaining gap beside cables can be filled with steel bricks
S. Girod BE-EA

## Slide 13: Proposed modifications
Today
Proposal
M2
M2
S. Girod BE-EA
Access chicane
modification

## Slide 14: Proposed modifications
6.4 m
7.2 m
M2
M2
absorber
Target
3.2 m
3.2 m
1.6 m
2.3 m
RP fenced door
M2
Front View
Side View
Top View
S. Girod BE-EA
Target Bunker

## Slide 15: Results from RP simulations
Prompt ambient dose equivalent rate (µSv/h) for 4.8 x 108 π-/spill and 240 spills/h on Target
Prompt annual ambient dose equivalent rate (mSv/h) for 3 x 1014 π-/year on Target
The beamline has been simulated in FLUKA with the proposed modifications.
Results show the proposed shielding design is in agreement with radiation area classification.
Air activation for access in EHN2 hall is negligible.
Annual activity in all air volumes is below 0.1 TBq/y for 3 x 1014 π-/year on target.
Exposure of members of the public due to air releases is below 0.1 µSv/y.
A. Devienne, C. Ahdida HSE-RP

## Slide 16: Results from RP simulations
The residual ambient dose equivalent rate has also been checked for 6-month irradiation at 4.8 x 108 π-/spill and 240 spills/h on target for a 2 minute cool-down and a 1h cool down time.
To optimise the access to the bunker a PMI monitor will be requested to monitor the residual dose rate inside the bunker before access.
A. Devienne, C. Ahdida HSE-RP

## Slide 17: Summary
For muon beams the rate is limited by the environmental radiation downstream of the EHN2 hall.
The maximal current average dose rate reached is ~ 1.9 µSv/h. Area classification limit at 2.5 µSv/h.
From the beamline considerations rate can be increase by another 40% by reducing the energy but limited by RP.
Measurement campaigns are planned with RP next year to study the optimal position of the environment monitors as this year already the doses registered were greater than in 2022 when SM1/SM2 were off during the high intensity MUonE run.
Shielding improvements does not apply for muons. Only mitigation will be extending the exclusion zone downstream of EHN2 or trying to deflect the muon beam downwards with some magnets, blowing up the beam more etc., - But gain to be estimated following the measurement next year.
For the higher hadron beam intensity of 109 hadrons per spill improved shielding studied by RP and to be implemented during LS3.