## Slide 1: Batch spacing optimization at SPS injection by Reinforcement Learning
M. Remta, S. Rezagholi, F. Velotti

## Slide 2: Contents
Motivation
Introduction
Environment
Algorithm
Results
Conclusion

## Slide 3: Motivation
For LHC-filling, multiple batches are injected into the SPS.
Batch spacing: gap between batches to pulse injection kickers.
SPS batch spacing 225 ns -> 200 ns: 6% increased luminosity in the LHC.
Notes: Introduction: Proton chain Multiple transfers of beam from SPS to LHC
Also, multiple injections into the SPS from PS. Batch spacing.

## Slide 4: The SPS injection system
16 injection kickers
  12 of type S.
  4 of type L.
  Fast-pulsed.
  Powered in pairs of two -> 8 circuits.
Eight independently controlled switches, one per circuit.
E. Waagaard, et al., "Design of a new CERN SPS injection system via numerical optimisation," JACoW IPAC2023, MOPA097 (2023). https://doi.org/10.18429/JACoW-IPAC2023-MOPA097

## Slide 5: Problem
Injection kicker rise time was designed for 225 ns spacing.
Flat-top ripples before stabilising.
Reduced spacing of 200 ns:
  Non-zero kick to the circulating beam.
  Insufficient deflection of the injected beam.
Both beams oscillate (injection oscillations):
  Filamentation.
  Halo population.

## Slide 6: Baseline
Initially, synchronisation of kickers was done manually [1]:
  Align waveforms according to time-of-flight.
  Shift waveforms to equalise oscillation amplitude of beams.
Replaced by numerical optimisation [2]:
  Bounded Optimisation by Quadratic Approximation (BOBYQA).
  Explores aggressively -> disruptive.
  In the median, 246 steps to converge.
  System drifts require re-running the algorithm.
Reinforcement learning as alternative.
[1] W. Bartmann, et al., "Impact of LHC and SPS Injection Kicker Rise Times on LHC Filling Schemes and Luminosity Reach," JACoW IPAC2017, TUPVA007 (2017). https://doi.org/10.18429/JACoW-IPAC2017-TUPVA007 [2] E. W. Waagaard, "Optimising the present and designing the future: a novel SPS injection system," Master's thesis, 2022. https://repository.cern/records/ra4pn-n7n17

## Slide 7: Goals for the RL agent
Optimiser: reach optimal working point from bad initial states.
Active controller: Maintain optimal working point when the system drifts.
Train exclusively in simulations:
  Beam time in the SPS is scarce.
  Avoid losing high-energy beam.
  Real system drifts slowly -> limited variation when training on the accelerator.

## Slide 8: Environment

## Slide 9: Overview

## Slide 10: Action space
Action space: change to delays a ∈ [-15 ns, 15 ns]8.
Delta-action approach: 𝜏i+1 = 𝜏i + ai.
Absolute actions were not robust to noise.
Optimised step size in simulations.

## Slide 11: Observation space
266 dimensions in total.
Current measured in each circuit -> waveforms.
33 datapoints per waveform, covering 264 ns.
Centred at the half-point between beams.
Waveforms normalised individually.
Amplitude of injection oscillations at a BPM downstream of the kickers.

## Slide 12: Reward
Loss function for numerical optimiser performed well.
Chose negated loss function as reward.

## Slide 13: Time horizon and terminal states
Artificial terminal states can create unwanted incentives.
Agent as active controller -> infinite horizon is the natural choice.
Drawback: agent can shift waveforms arbitrarily far.
Machine protection: terminal states?
  Beam loss.
  Boundary on absolute settings 𝜏.
  Reward goal.
Solution: no terminal states
  Truncation in training.
  Shielding during inference.
negative reward -> terminate asap.
}

## Slide 14: Training environment
Simulation of the real machine.
Truncate episodes after 1000 steps.
Waveform data:
  100 sets of measurements.
  Augmentation: randomly increase rise times up to 20%.
Randomise initial settings:
  Global shift u ~ N(0, 10 ns).
  Individual shift vi ~ N(0, 5 ns).
2nd-order transfer matrices from injection region to BPM.

## Slide 15: Partial observability
Arrival time of beams is estimated.
Waveforms measurements might not be perfectly synchronised.
Apply hidden shifts in simulations:
  Global shift: δ ~ U(-20 ns, 20 ns)
  Individual shift: ε ~ U(-15 ns, 15 ns)

## Slide 16: Algorithm

## Slide 17: Proximal Policy Optimisation (PPO)
Stochastic policy: actions are drawn from a distribution.
Policy network: outputs parameters of distribution.
Policy update is clipped to prevent large changes.

## Slide 18: PPO + LSTM
Equip agent with memory to solve the partially observable environment.

## Slide 19: Training & Hyperparameters
Training budget: 106 steps.
Hyperparameter tuning:
  Discount factor
  Training parameters
  Network architecture

## Slide 20: Results

## Slide 21: Simulations
 | RL agent | Numerical Optimiser
Steps until converged | 7 | 246
Benchmarked agent against BOBYQA on 104 episodes.
Agent performs on par with optimiser.
x35 speed-up
Agent optimises significantly faster.

## Slide 22: Dedicated study (2024)
Agent tested as active controller.

## Slide 23: SPS commissioning (2026)
Deployed the same agent as optimiser.
Improved, but unbalanced
Manual intervention

## Slide 24: SPS commissioning (2026)
Deployed the same agent as optimiser.
Improved, but unbalanced

## Slide 25: SPS commissioning (2026)
Deployed the same agent as optimiser.
Manual intervention

## Slide 26: Simulation-reality-gap
Inversion of discrepancy hints at global shift.

## Slide 27: Conclusion
Train exclusively in simulations ✅
Active controller ✅
Optimiser (✅)
Learnings:
  Diverse experience in training.
  Simulated partial observability.
  Agents with memory.
Future work:
  Match simulations to accelerator.
  Translation invariant observation space.

## Slide 28
Paper
Repository

## Slide 29: Backup

## Slide 30: Historical rise times

## Slide 31: Step size study: PPO hyperparameter

## Slide 32: Hyperparameter: LSTM-PPO