## Slide 1: Extending RL with BO and Online Sys Id for SPS-North Area Beam Commissioning
Presenter: Adrián Menor de Oñate Acknowledgements: Michael Schenk, Verena Kain, Borja Rodriguez Mateos, Niky Bruchon, Nikolaos Charitonidis, Giovanni Dal Maso, Alexander Huschauer, SPS OP 25-03-2026
Notes: Part of the NA beam commissioning.

## Slide 2: The SPS-North Area Transfer Lines
Goal: Having an aligned beam in the transfer lines, and target efficiency
Act via dipole magnets (correctors), and movable monitors
Observations?

## Slide 3: Observation Challenges
There are no conventional beam position monitors available!
Split foils (BSPs) are used instead
Classical control algorithms (currently used) fail when the beam is only on one foil
Beam
Foil

## Slide 4: Commissioning the Beam
Severe Misalignment Steering
High Symmetry Steering
Polarity Estimation
Optimisation of the Targets
How do we approach this complex automation?
Do we just use RL for everything?
RL

## Slide 5: Problem Specifications
Operational testing time is limited to ~2 times per year
Automation solution must allow for performing the different commissioning activities
The different commissioning automations must be independently testable
  Limiting complexity is key

## Slide 6: Building an Automation Solution
SPS
NA
Controls
Interfaces
Autopilots
BO
RL
Automated SPS-NA beam commissioning

## Slide 7: Commissioning the Beam
Severe Misalignment Steering
High Symmetry Steering
Polarity Estimation
Optimisation of the Targets
RL

## Slide 8: Steering From Severe Misalignment

## Slide 9: Steering from Severe Misalignment
Beam can be completely off the foils (BSPs)
SPS Beam
!
!
!
Corrector
BSP
BSP

## Slide 10: Steering from Severe Misalignment
Beam can be completely off the foils (BSPs)  Beam threading
SPS Beam
!
!
!
Corrector
BSP
BSP
Segment 1
Segment 2
Segment 3

## Slide 11: Steering from Severe Misalignment
Beam can be completely off the foils (BSPs)  Beam threading
SPS Beam
!
Corrector
BSP
BSP
Segment 1

## Slide 12: Steering from Severe Misalignment
Segment 2
Beam can be completely off the foils (BSPs)  Beam threading
SPS Beam
!
Corrector
BSP
BSP

## Slide 13: Steering from Severe Misalignment
Segment 2
Beam can be completely off the foils (BSPs)  Beam threading
SPS Beam
Corrector
BSP
BSP

## Slide 14: Steering from Severe Misalignment
Segment 3
Beam can be completely off the foils (BSPs)  Beam threading
SPS Beam
Corrector
BSP
BSP

## Slide 15: Steering from Severe Misalignment
Segment 3
Beam can be completely off the foils (BSPs)  Beam threading
SPS Beam
Corrector
BSP
BSP

## Slide 16: Steering from Severe Misalignment
Beam can be completely off the foils (BSPs)  Beam threading
SPS Beam
Corrector
BSP
BSP
SPS Beam
Corrector
BSP
BSP

## Slide 17: Design Choices
Could use RL but…
  Corrector polarities are not known
  The exploration strategies for this problem are already known
  We don’t want to train online, machine time matters
  Other (simpler) schemes work too
Try corrector settings until putting the beam on the foils, then get a sample efficient picture of the optimization landscape and optimize symmetries

## Slide 18: Bayesian Optimization
Actions are relative
First do quasi random actions
Then Bayesian optimization
Gaussian Process (GP) Model
Acquisition Function
Transfer Line
+
New data

## Slide 19: BO Results
31st of March 2026

## Slide 20: Threading the TT21 H Line
Full line steered from severe misalignment
Low intensity beams, noisy measurements, but safer for the machine
During the test, the optimizer took ~15 minutes to optimize the full line (compared to potentially hours of manual tuning)
20
31st of March 2026

## Slide 21
Threading the TT21 H Line
21
31st of March 2026

## Slide 22: Commissioning the Beam
Severe Misalignment Steering
High Symmetry Steering
Polarity Estimation
Optimisation of the Targets
RL
BO + Quasi Random Search

## Slide 23: Commissioning the Beam
Severe Misalignment Steering
High Symmetry Steering
Polarity Estimation
Optimisation of the Targets
RL
BO + Quasi Random Search

## Slide 24: Polarity Estimation

## Slide 25: Design Choices
Could use RL but…
  Optimization setup becomes complex (reward function?)
  Simpler methods (kick response) are simpler, more maintainable
We need a sample efficient identification of the polarities

## Slide 26: Algorithm
Kick response on the correctors
Changes in BSPs are compared against simulation model
Corrector
Corrector
BSP
MDAH.2303
26
31st of March 2026

## Slide 27: Algorithm
BSP
27
Corrector
Corrector
Kick response on the correctors
Changes in BSPs are compared against simulation model
31st of March 2026

## Slide 28: Algorithm
MDAH.2303
MDAH.2307
BSP
28
Corrector
Corrector
Kick response on the correctors
Changes in BSPs are compared against simulation model
31st of March 2026

## Slide 29: Reality
MDAH.2303
MDAH.2307
29
During the test, the optimization took ~7 minutes to identify all the polarities
31st of March 2026

## Slide 30: Test Results
MDAH.2303
MDAH.2307
30
Corrector | 2101 | 2102 | 2106 | 2109 | 2112 | 2113 | 2115
Run 1 |  |  |  |  |  |  | 
Run 2 |  |  |  |  |  |  | 
7/7 (100%)
6/7 (86%)
31st of March 2026

## Slide 31: Commissioning the Beam
Severe Misalignment Steering
High Symmetry Steering
Polarity Estimation
Optimisation of the Targets
RL
BO + Quasi Random Search
Kick Response
31st of March 2026

## Slide 32: Commissioning the Beam
Severe Misalignment Steering
High Symmetry Steering
Polarity Estimation
Optimisation of the Targets
RL
BO + Quasi Random Search
Kick Response
31st of March 2026

## Slide 33: Steering the Line for High Symmetry
31st of March 2026

## Slide 34: Design Choices
Can we use RL here?…
  Corrector polarities are known
  Designing a controller to tradeoff symmetries at the different monitors for high target symmetry is complex  can use RL to discover control strategies
  Accurate simulation model allow for training offline
Need to steer the line to a high symmetry, even from situations where the beam is in one foil only
31st of March 2026

## Slide 35: Reinforcement Learning Setup
Dipoles’ settings
31st of March 2026
More info in the poster!

## Slide 36: RL Results
31st of March 2026

## Slide 37: Simulation
31st of March 2026

## Slide 38: Reality
31st of March 2026

## Slide 39: Commissioning the Beam
Severe Misalignment Steering
High Symmetry Steering
Polarity Estimation
Optimisation of the Targets
RL
BO + Quasi Random Search
Kick Response
31st of March 2026

## Slide 40: Commissioning the Beam
Severe Misalignment Steering
High Symmetry Steering
Polarity Estimation
Optimisation of the Targets
RL
BO + Quasi Random Search
Kick Response
31st of March 2026

## Slide 41: Optimizing the Targets
31st of March 2026

## Slide 42: Optimizing the Targets
SPS Beam
Target
BSM = movable split monitor
TBIU = target beam instrumentation upstream
BSM
TBIU
SPS Beam
Target
BSM
TBIU
31st of March 2026
Notes: Explain how we wait for the YASP autopilot to steer.

## Slide 43: Design Choices
We could use RL but…
  RL system is complex (hierarchical, multi-objective, etc)
  Need a system that can swiftly adapt to different target configurations (number of scintillators, etc)
  We can simply act in a modular way from what we already have
Need to find the optimum BSM, TBIU positions while we keep steering for high symmetry at the targets
31st of March 2026

## Slide 44: Automating The Target Setup
Steering Algorithm (RL, etc)
BSM = movable split monitor
TBIU = target beam instrumentation upstream
31st of March 2026

## Slide 45: Test Results
Optimization of both setups
31st of March 2026

## Slide 46: Commissioning the Beam
Severe Misalignment Steering
High Symmetry Steering
Polarity Estimation
Optimisation of the Targets
RL
BO + Quasi Random Search
Kick Response
BO
31st of March 2026

## Slide 47: Conclusion
SPS
NA
Controls
Interfaces
Autopilots
BO
RL
Automated SPS-NA beam commissioning
RL is a great tool to discover control policies
It can come at the cost of complexity, slow learning online, and maintainability
Properly using it in complex automations is challenging and essential
31st of March 2026

## Slide 49: Backup slides

## Slide 50: Reinforcement Learning Setup
Dipoles’ settings
Example
March 25ᵗʰ 2026

## Slide 51: Reward Function
Centered beam
No beam loss
March 25ᵗʰ 2026

## Slide 52: Reinforcement Learning Agent
TD3 algorithm
Hindsight Experience Replay (HER) buffer
  Robust against sparse reward functions
  Implicit curriculum learning
Image: Packer, C., Abbeel, P., & Gonzalez, J. E. (2021). Experience Replay for Sparse Reward Meta-RL. 35th Conference on Neural Information Processing Systems (NeurIPS 2021).
March 25ᵗʰ 2026

## Slide 53: Hindsight Experience Replay (HER)
Train with larger actions and harder stopping criteria
No need for curriculum learning
HER
W/O HER
March 25ᵗʰ 2026

## Slide 54: Reality
March 25ᵗʰ 2026

## Slide 55: Reality

## Slide 56: Reality
Before
After

## Slide 57: Simulation vs Reality
 | Simulation | Reality
Beam loss flag | Mean beam position | Intensity threshold
Noise | Initial magnet settings | Magnet settings, beam conditions etc

## Slide 58: Conclusion
The RL policies successfully transfer to the real world
The beam can be successfully steered in the different tests
The RL pipeline is flexible to adapt to the different transfer lines

## Slide 59: Bringing the Beam Back

## Slide 60: Algorithm
Sequential choice of correctors (one corrector at a time)
Perturbation actions are sent to the given corrector (sending )
Expected changes in BSPs are computed with MADX model and compared against machine reading
Polarities are estimated inspecting the correlation of such comparisons
MDAH.2303
MDAH.2307
BSP
MDAH.2303
March 25ᵗʰ 2026
60

## Slide 61: Algorithm
Sequential choice of correctors (one corrector at a time)
Perturbation actions are sent to the given corrector (sending )
Expected changes in BSPs are computed with MADX model and compared against machine reading
Polarities are estimated inspecting the correlation of such comparisons
MDAH.2303
MDAH.2307
BSP
March 25ᵗʰ 2026
61

## Slide 62: Algorithm
Sequential choice of correctors (one corrector at a time)
Perturbation actions are sent to the given corrector (sending )
Expected changes in BSPs are computed with MADX model and compared against machine reading
Polarities are estimated inspecting the correlation of such comparisons
MDAH.2303
MDAH.2307
MDAH.2303
MDAH.2307
BSP
March 25ᵗʰ 2026
62