## Slide 1: UBT Straws
University of Liverpool
18/9/25
T. Bowcock

## Slide 2: Short Message
Understand the problem
Apply the technology
Build & Test Prototype
Optimize….

## Slide 3: What do SHiP want?
0 Material detector DIRECTLY after Muon Shield
  Before He Volume
  Before what was the SND (neutrino detector)
3x1m area (!)
Tracking/VETO
What physics benefit (cost)?

## Slide 4: Straws
See talk in Zürich (May)
  Updates
A quick recap of what we know
  Cheap
  Efficient
  Capable of O(<50 μm track resolution)
  Can be built “light” or “heavy”, “small or large” (more later)
  Pretensioning can be an issue (more later)
  QA/QC critical
  Takes about 1 year to build a 3000 straw tracker
    Design for SHiP would be faster

## Slide 5: Pretensioning mu2e
Four different initial tension of 300, 400, 500 and 600 gram-meter (gm) were ap plied to 120 cm long straws
An extrapolation of measured tension data results that O(600) gm initial tensioning is required to get > 200 gm tension after life time operation of straw.
Test for 5 years

## Slide 6: Why is this important?
Wires need to be tensioned
  SEPARATELY
  FRAME AND WIRE CAN MATCH EXPANSION (3ppm)
Straws Usually Tensioned
Differential Expansion (T)
  Straw 20ppm
Humidity
Tensioning keeps straw geometry aligned with wire
Can you retain geometry (e.g. under pressure) and wire tension WITHOUT extreme tension??
  1000*500g=0.5 Tonne
  Stiff and strong frame!!
Secondary enclosure?
  R&D?

## Slide 7: Performance
Efficiency – ~97-98% over all straw (99% best)
Resolution O(100 μm/layer)
Voltage – 1650V
Lifetime – no degradation at all seen
Leakage – maintain better than 10-9 torr in region of detectors
Operated in 2T field

## Slide 8: For SHiP
Build O(1.2 m) detector with 5mm straw.
Each plane a double one for efficiency (2 layers per plane)
  Split into 3 submanifolds of 128 (64 in each layer?)
Arranged “vuw” (0, 60, 120,0,60, 120?)
  Julich Configuration
O(2300) straws
Straw length about 1150mm
  To be tuned for radiation profile
Wire Pretensioning problem
  Engineers suspension bridge
  Partially Solved by using composite frame
  Tuned to Tungsten Rhenium +Epoxy

## Slide 9: Propose (Sep)
6mm separation
64*6=384 mm
Each manifold 128 straws
Double layer

## Slide 10: To understand/calculate
Max load on each CF frame >> tensioning
Match wire and frame CTE (“easy”)
Influence of straw creep
Environment (Radiation)
Physics Requirements
Precise Requirements on Detector Resolution etc.

## Slide 11
ZURICH MODEL

## Slide 12: Improved (slightly). Support. Holes.
0 °
60 °
120 °

## Slide 13
Cost O(0.5M)

## Slide 14: Large Area Silicon Tiles (FYI)
We have just had delivered (to be tested 2025) – 150kChf development
New design – 10cm x 10cm tile
  From Micron Semiconductor
Can be rad hard (or not!!)
50 micron readout (with intermediate strip) 1990s technology
Designed for < 5 micron resolution
We could instrument with these
  Once we have the ASIC!!!!
  2025 Addon!!

## Slide 15
CMS 2S Modules

## Slide 16: Summary(1)
Understanding environment
Looking at allocating effort for MC
With ASIC we think this can be built in 1 year (once we know our parameters)
We propose for cost/effort/tooling retaining 5mm straws.

## Slide 17: But this not good enough!!
Basically
  3x1 area is needed to be instrumented and clear (not just core)
  No material in centre (manifolds, structure)
  Building long vertical straws (a la ATLAS TRT is HARD)
    FCCee
Can we save the 1.3x1.3module we could build now?

## Slide 18: Strawman
Multiple 1m2 modules
Horizontal Straws
  No manifolds in volume
But how do we keep the tension O(0.2-.5tonne) on straws without building giant frame
Assume we do NOT want to build big fram

## Slide 19: Idea -
Build identical modules similar to Zurich Design
Design so when installed (onto the Muon Shield?) the horizontal tension strut can be removed
Build/Transport
Install
Remove tension struts
This in inscreases cost (0.1M)

## Slide 20: Summary
Don’t reinvent the (SHiPs) wheel!
If we don’t worry about detector mass makes life easier
  Probe tensioning options.
  NOTE CF frames have real advantages
Spiral v Laminar – choose what is available
  We are predisposed to spiral as its an “old friend” and robust.
PROTOTYPE
Establish QA/QC
If we need large area precision (£) Si – we are working on it!!
  MuonE
  We would propose to add a few planes to straws in high rate overlap region
WE NEED TO UNDERSTAND PHYSICS/BENEFIT

## Slide 21: Backup

## Slide 23
The Julich arrangement “tends” to avoid the high radiation/rate areas.

## Slide 24: 5mm straws
2 layers (6 microns, 3 microns of glue) – spiral wound
Wire 25μm Tungsten Rhenium
Ar:C₂H₆ 50:50; chosen for gain plateau & low leak rate through aluminized Mylar
Straws operated in vacuum and tested in 1.2 m lengths (0% leak/burst)
“Double helix” of ~6 µm Mylar with ~3 µm adhesive (≈15 µm total) inner surface 500 Å Al + 200 Å Au (cathode) outer surface 500 Å Al (shielding & reduced permeation)
Mylar (PET) (less soft than Kapton)
Young’s modulus: ~4–6 GPa
Tensile strength: ~150–200 MPa
Elongation at break: ~100–120%
At 1atm expansion O(10um)
Operate at <10% of elastic yield
Mu2e shows O(100um) creep over 10years . Double layer helps. Prestress.

## Slide 25: One end
Toleranced to microns
Pin (annealed)
Al ( one end with lip)
Straw ends here (OD Al 30um larger than straw)
Plastic insert
WE HAVE ESTABLISHED ALL TOOLING EXISTS BOTH AT LIVERPOOL AND IN COMPANIES THAT MAKE PARTS

## Slide 26: Tooling etc
Everything built to O(10um). Propose to retain this precision.

## Slide 27: Commentary
Everything databased and qualified individually
  Wires, pins, straws (precision parts used)
  Aligned and metrologized to 10 microns
    Precision manifolds and careful work
  CLEAN ROOM => NO HV TRAINING EVER NEEDED
    Clean procedures and training
  To my knowledge not even 1 spark over 6-8 years of prototype/operation
  This is good starting point
Need to establish operating conditions (MHz, composition…)
We can confidently cost materials (exc electronics ) 150K.

## Slide 28: Spiral Tubes
No long straight seam → stresses are distributed helically, not concentrated.
Redundancy: even if one seam leaks slightly, the second offset layer helps maintain gas integrity.
Proven technology: used successfully in ATLAS TRT, Mu2e, g-2.
Manufacturing is scalable (Paramount Tube and similar vendors can mass-produce).
Survive 1atm differential easily
Helical seam leads to slight periodic non-uniformities in wall thickness and surface.
More material (≈15 μm total wall vs. thinner possible with welded), slightly worse radiation length.
Adhesive layers can age/outgas.
Field symmetry is not perfect (we found this negligible)