## Slide 1: Single-shot electron bunch profile monitor based on coherent transition radiation imaging
1. Department of Physics, University of Liverpool, Liverpool L69 7ZX, UK
2. Cockcroft Institute, Sci-Tech Daresbury, Daresbury WA4 4AD, UK
3. MAX IV Laboratory, Lund University, Lund 224 84, Sweden
Ana Guisao-Betancur1,2, Joseph Wolfenden1,2, Erik Mansten3, Sara Thorin3, Johan Lundquist3, Oliver Grimm3, Carsten Welsch1,2
A.M.Guisao-Betancur@liverpool.ac.uk

## Slide 2: Content overview
Problem description
Transition radiation-based monitor
Designing for a short-pulse facility
Results and discussion
Next steps
References
----------------------------------------------------------------------------------------------------------------------------------------------

## Slide 3: 1. Problem description
Need for monitoring ultrashort electron bunches in the femtosecond range
In the case of EuPRAXIA and other short-pulse accelerators, bunch lengths can be sub-fs to a few hundreds of fs long. This brings a challenge for the development of longitudinal diagnostics.
Plasma-based accelerators can produce ultra-short electron bunches and impart energy gain of several GeV with accelerating distances of only few centimeters.
Figure 1. Wakefield generation and electron beam acceleration in a plasma accelerator showing the behavior in a laser-driven plasma (wakefield) accelerator (LWFA) .
Parameter | Range of exploration
Bunch length (FWHM) | 
Energy | 
Bunch charge | 
Repetition rate | 
Normalised emittance | 
Energy spread | 
Parameter | Range of exploration
Bunch length (FWHM) | 
Energy | 
Bunch charge | 
Repetition rate | 
Normalised emittance | 
Energy spread | 
Table 1. Summary of the electron beam properties for EuPRAXIA (at entrance of undulator for FEL).
Assmann, R. W. et al. EuPRAXIA Conceptual Design Report. Eur. Phys. J. Spec. Top. 229, 3675–4284 (2020).

## Slide 4: 2. Transition radiation-based monitor
About generation of (coherent) transition radiation
Figure 2. Transition radiation generation scheme.
Transition radiation (TR) is produced when charged particles pass a boundary between two media with different dielectric properties.
It is typically broadband, from microwave to X-ray, depending on the particles' energy and the media's properties. It is coherent (CTR) when
.
For relativistic particles (), the radiation is emitted in a narrow cone around the direction of particle propagation.
Figure 3. Simulated spectral intensity of TR emitted by an unstructured, Gaussian-distributed electron bunch with charge, energy and (FWHM) duration.
Zarini, O. et al. Multioctave high-dynamic range optical spectrometer for single-pulse, longitudinal characterization of ultrashort electron bunches. Phys. Rev. Accel. Beams 25, 1–19 (2022).
Spectrometer
Imaging system
Commonly studied with
Our approach
Detector position | Image plane
Image information | Point-to-point spatial distribution of the TR source

## Slide 5: 2. Transition radiation-based monitor
Working principle: CTR spatial distribution image and longitudinal bunch profile
CTR image (from a bunch)
No. of e-
Bandwidth
Single e- spectral image
Longitudinal form factor
Sample of simulated CTR image
(spatial distribution)
Where:
Contains information about the particle distribution or bunch longitudinal profile:
Assuming transverse coherence condition on the beam size
Shkvarunets, A. G. & Fiorito, R. B. Vector electromagnetic theory of transition and diffraction radiation with application to the measurement of longitudinal bunch size. Phys. Rev. Spec. Top. - Accel. Beams 11, 012801 (2008).
Wolfenden, J. et al. Coherent Transition Radiation Spatial Imaging As a Bunch Length Monitor. in 10th Int. Particle Accelerator Conf. 2713–2716 (2019).

## Slide 6: 2. Transition radiation-based monitor
Working principle: previous work
Sample of simulated CTR image
(spatial distribution)
Figure 5. Demonstration of FWHM distance variation with bunch length in CTR image distributions.
CTR image parameters such as the peak-to-peak distance or the image width (FWHM) show dependence on the bunch length.
TPX lens 2f-2f imaging system
Figure 4. Simulated 1D cross-sections of the absolute (a) and normalized (b) spatial distribution of a CTR image from a for a range of Gaussian longitudinal bunch profiles.
Wolfenden, J. et al. First demonstration of coherent radiation imaging for bunch-by-bunch longitudinal compression monitoring. Submitted to Phys. Rev. Accel. Beams (2025).
Examples of measured images
Figure 6. CTR image FWHM variation with K01 and K02 phase.
@ MAX IV SPF

## Slide 7: 3. Designing for a short-pulse facility
Identifying the requirements for the MAX IV short pulse facility (SPF)
Figure 7. Targeted system location at the MAX IV SPF.
Parameter | Value / range
Bunch length (FWHM) | 
RMS transverse size | few
Energy | 
Bunch charge | 
Repetition rate | 
Normalised emittance | 
Energy spread | 
Parameter | Value / range
Bunch length (FWHM) | 
RMS transverse size | 
Energy | 
Bunch charge | 
Repetition rate | 
Normalised emittance | 
Energy spread | 
Requirement for an imaging system covering
Table 2. Electron beam parameters at the SPF (and CTR location).
at
Transverse coherence condition

## Slide 8: 3. Designing for a short-pulse facility
Off-axis parabolic (OAP) mirrors
RFL=4”
RFL=8”
Protected silver coating
Design of the acquisition system: description of the components
Figure 8. Schematic of the CTR imaging system.
e-beam
Vacuum viewport window
High resistivity float zone silicon (HRFZ-Si)
Pyrocam
2x magnification
CTR spatial image
Pyrocam™ IIIHR GigE 160x160 px
13 to 355 nm and 1.06 to 3000 μm
TR target
The beam is strongly scattered at this thickness.
A less invasive setup could be achieved with a thinner target (few tens ).
These will modulate the resulting image.
Figure 9. Optical properties for the elements on the imaging system.

## Slide 9: 4. Results and discussion
Monitor location and installation
Figure 11. CTR imaging system at SP02.
Compact system
Figure 10. SPF data collection positions.
CTR images’ location
Transverse deflecting cavity (TDC) for reference measurements

## Slide 10: 4. Results and discussion
Data collection: CTR image acquisition and reference bunch profile data
160x160 px
Figure 12. CTR sample phase scan at linac L1.
Figure 13. TDC reference phase scan at linac L1.

## Slide 11: 4. Results and discussion
First look at the CTR images: CTR image analysis & bunch length
2x magnification
Figure 14. Methodology for CTR image analysis.
Single-shot
Examples of CTR images to be analysed.
Horizontal image profiles obtained by summing pixel values vertically, fitted to Gaussians, and FWHM extracted (feature used for analysis).
Vertical image profiles.

## Slide 12: 4. Results and discussion
Preliminary direct analysis of the spatial images
Figure 15. Analysis for a 1D phase scan at linac L1.
Visible CTR images within the scan range that are valid for performing the posterior analysis.
Reference bunch length variation through the phase scan from TDC measurements, reaching a point of maximum compression or waist.
Results from the CTR image analysis, which feature the FWHM changes for the image profiles in both horizontal (green) and vertical (blue) dimensions, as well as the total image intensity (red), all suggest an analogous behaviour of the bunch passing through a waist, as depicted in the reference data from (b).

## Slide 13: 5. Next steps
(A) Direct comparisons using simulated CTR images to get a rigorous characterization of the CTR image distributions and the corresponding bunch lengths.
Understanding further the CTR images
Next steps
Figure 16. Experimental and simulated data comparisons.
same FWHM
different bunch profile “shape”
different CTR images
+
=
How certain features of the bunch profile translate to the CTR image.

## Slide 14: 5. Next steps
Convolutional neural networks (CNNs)
Extension to bunch profile reconstruction
(B) Extend to bunch profile reconstruction from the whole CTR image using deep learning.
Works for simulated CTR images for sums of Gaussian profiles.
Currently working with the experimental dataset.
experimental CTR images
reference bunch profiles from the TDC
Next steps
Figure 17. Bunch profile reconstruction deep learning workflow.

## Slide 15: References
----------------------------------------------------------------------------------------------------------------------------------------------
R. W. Assmann et al., “EuPRAXIA Conceptual Design Report,” Eur. Phys. J. Spec. Top., vol. 229, no. 24, pp. 3675–4284, Dec. 2020, doi: 10.1140/epjst/e2020-000127-8.
M. C. Downer, R. Zgadzaj, A. Debus, U. Schramm, and M. C. Kaluza, “Diagnostics for plasma-based electron accelerators,” Rev. Mod. Phys., vol. 90, no. 3, p. 35002, 2018, doi: 10.1103/RevModPhys.90.035002.
Curcio et al., “Non-invasive bunch length measurements exploiting Cherenkov diffraction radiation,” Phys. Rev. Accel. Beams, vol. 23, no. 2, p. 22802, 2020, doi: 10.1103/PhysRevAccelBeams.23.022802.
Davut et al., “Design and experimental verification of a bunch length monitor based on coherent Cherenkov diffraction radiation,” Phys. Rev. Res., vol. 7, no. 1, p. 13193, 2025, doi: 10.1103/PhysRevResearch.7.013193.
H. Yamada et al., “Study of Coherent Smith–Purcell Radiation in the Terahertz Region Using Ultra-Short Electron Bunches,” Particles, vol. 6, no. 3, pp. 693–702, 2023, doi: 10.3390/particles6030042.
B. Schmidt, N. M. Lockmann, P. Schmüser, and S. Wesch, “Benchmarking coherent radiation spectroscopy as a tool for high-resolution bunch shape reconstruction at free-electron lasers,” Phys. Rev. Accel. Beams, vol. 23, no. 6, p. 62801, 2020, doi: 10.1103/PhysRevAccelBeams.23.062801.
N. M. Lockmann, C. Gerth, B. Schmidt, and S. Wesch, “Non-invasive THz spectroscopy for bunch current profile reconstructions at MHz repetition rates,” Phys. Rev. Accel. Beams, vol. 23, no. 11, p. 112801, 2020, doi: 10.1103/PhysRevAccelBeams.23.112801.
S. Wesch, B. Schmidt, C. Behrens, H. Delsim-Hashemi, and P. Schmüser, “A multi-channel THz and infrared spectrometer for femtosecond electron bunch diagnostics by single-shot spectroscopy of coherent radiation,” Nucl. Instruments Methods Phys. Res. Sect. A Accel. Spectrometers, Detect. Assoc. Equip., vol. 665, pp. 40–47, 2011, doi: 10.1016/j.nima.2011.11.037.
M. Heigoldt et al., “Temporal evolution of longitudinal bunch profile in a laser wakefield accelerator,” Phys. Rev. Spec. Top. - Accel. Beams, vol. 18, no. 12, pp. 1–6, 2015, doi: 10.1103/PhysRevSTAB.18.121302.
S. I. Bajlekov et al., “Longitudinal electron bunch profile reconstruction by performing phase retrieval on coherent transition radiation spectra,” Phys. Rev. Spec. Top. - Accel. Beams, vol. 16, no. 4, pp. 1–14, 2013, doi: 10.1103/PhysRevSTAB.16.040701.
O. Zarini et al., “Multioctave high-dynamic range optical spectrometer for single-pulse, longitudinal characterization of ultrashort electron bunches,” Phys. Rev. Accel. Beams, vol. 25, no. 1, pp. 1–19, 2022, doi: 10.1103/PhysRevAccelBeams.25.012801.
F. G. Bisesto, M. Castellano, E. Chiadroni, and A. Cianchi, “Zemax simulations describing collective effects in transition and diffraction radiation,” Opt. Express, vol. 26, no. 4, p. 5075, 2018, doi: 10.1364/oe.26.005075.
J. Wolfenden, C. P. Welsch, T. H. Pacey, and A. Shkvarunets, “Coherent Transition Radiation Spatial Imaging As a Bunch Length Monitor,” pp. 2713–2716, 2019, doi: 10.18429/JACoW-IPAC2019-WEPGW095.
A. G. Shkvarunets and R. B. Fiorito, “Vector electromagnetic theory of transition and diffraction radiation with application to the measurement of longitudinal bunch size,” Phys. Rev. Spec. Top. - Accel. Beams, vol. 11, no. 1, p. 012801, Jan. 2008, doi: 10.1103/PhysRevSTAB.11.012801.
V. E. Rogalin, I. A. Kaplunov, and G. I. Kropotov, “Optical Materials for the THz Range,” Opt. Spectrosc., vol. 125, no. 6, pp. 1053–1064, 2018, doi: 10.1134/S0030400X18120172.
S. Sung et al., “THz optical design considerations and optimization for medical imaging applications,” Terahertz Emit. Receiv. Appl. V, vol. 9199, p. 91990S, 2014, doi: 10.1117/12.2062403.
C. Brückner, G. Notni, and A. Tünnermann, “Optimal arrangement of 90° off-axis parabolic mirrors in THz setups,” Optik (Stuttg)., vol. 121, no. 1, pp. 113–119, 2010, doi: 10.1016/j.ijleo.2008.05.024.
N. Chopra and J. Lloyd-Hughes, “Optimum Optical Designs for Diffraction-Limited Terahertz Spectroscopy and Imaging Systems Using Off-Axis Parabolic Mirrors,” J. Infrared, Millimeter, Terahertz Waves, vol. 44, no. 11–12, pp. 981–997, 2023, doi: 10.1007/s10762-023-00949-8.

## Slide 16: Thank you!
Any questions?
Ana Guisao-Betancur1,2, Joseph Wolfenden1,2, Erik Mansten3, Sara Thorin3, Johan Lundquist3, Oliver Grimm3, Carsten Welsch1,2
A.M.Guisao-Betancur@liverpool.ac.uk
1. Department of Physics, University of Liverpool, Liverpool L69 7ZX, UK
2. Cockcroft Institute, Sci-Tech Daresbury, Daresbury WA4 4AD, UK
3. MAX IV Laboratory, Lund University, Lund 224 84, Sweden