## Slide 1: Activity on g-2 in the UK
  Saskia Charity
  Muon Precision Physics Workshop @ Liverpool
  09 November 2022

## Slide 2
g-2 in the UK
Very active g-2 community in the UK
Major hardware contribution: straw tracking detectors (hardware, DAQ, tracking software)
Critical contributions and leadership in all major analysis areas of g-2 experiment
  Muon precession analysis, tracking analysis, beam dynamics, magnetic field, EDM, …

## Slide 3
How to measure g-2
Muon precession frequency
Magnetic field (proton Larmor frequency)

## Slide 4
How to measure g-2

## Slide 5
Tracking detectors
Two in-vacuum tracking stations at 180 and 270
One station = 8 modules
One module = 128 gas-filled straws, arranged in 4 layers
Measure trajectory of decay e+ to reconstruct muon beam profile
128 straws
10 cm long
15 um Al-coated mylar

## Slide 6
Straw tracker design & performance
Low mass (reduce multiple scattering) – 15 μm wall thickness; material < 0.5% radiation length
Low leak rate to satisfy vacuum requirement (<10-6 Torr); vacuum load < 10-5 Torr L/s
Tracking in non-uniform, varying magnetic field
Hit resolution of (110 ± 20) μm
Highly efficient across straw
Full details in B.T. King et al 2022 JINST 17 P02035
Radial B field in tracker region
Detection efficiency vs distance to wire

## Slide 7
Tracking detectors: Hardware
Electronics & DAQ: UCL, Boston University
Hardware design, QA and assembly at Liverpool
Wire stringing
CMM metrology
Readout electronics (ASDQs)
Leak testing
DAQ chain

## Slide 8
Tracking detectors: Software
Track finding: group hits in time and identify track candidates
Track fitting: uses GEANE method for chi-squared minimisation – direct access to full geometry and magnetic field map
Track extrapolation: Runge-Kutta Nystrom method – extrapolate track vector to muon decay position (point of radial tangency)
Wire stringing
CMM metrology

## Slide 9
Beyond Run-1: Track efficiency improvements
Wire stringing
CMM metrology
In Run-1: track quality more important than statistics -- very stringent quality cuts meant low percentage of recorded tracks used in analysis
In future, want to improve this efficiency – important for EDM analysis
Revised quality selection procedure: largest gains from cutting hits with large residuals that caused poor p-value for ‘good’ tracks
Requires reprocessing tracks for all datasets
  Running on GridPP nodes
Work by Gavin Hesketh & Lucy Bailey (UCL)

## Slide 10
Beyond Run-1: Machine Learning techniques for tracking
Wire stringing
CMM metrology
Readout electronics (ASDQs)
New approach: use ML techniques to improve track finding – particularly good for pileup events
Use overlaid selection of well-fitted, isolated tracks from data as training sample
Work by Anthony Hibbert & Joe Price (Liverpool)

## Slide 11
Trackers & Beam Dynamics in g-2
N(t) = number of muons in calorimeters vs time
Residuals in FFT if only 5 parameters used
Full fit function contains 26 parameters to account for beam dynamics and detector acceptance
5-parameter fit

## Slide 12
Beam dynamics with the tracker data
Measure oscillations in the radial and vertical beam distribution throughout a muon fill
Frequency/amplitude of oscillations in mean and RMS  input to ωa fit
Average muon beam position over long times used to weight the magnetic field measurement

## Slide 13
Corrections to ωa in Run-1: pitch correction Cp
Muon beam has vertical spread
Muons “pitch” up and down as they traverse the storage ring
Muons with momentum component parallel to B field have reduced precession frequency
Measured vertical distribution used to quantify correction
Cp = 180 (13) ppb (Run-1)

## Slide 14
Beyond Run-1: Muon precession analysis using trackers
Wire stringing
CMM metrology
Tracker measurement of ωa allows cross-check with calorimeter analysis with independent systematics
Anticipate BNL-level precision with full statistics (Runs 1-5) and updates to tracking algorithm & efficiency
Plots from George Sweetmore (Manchester)

## Slide 15
Muon-weighted magnetic field
Wire stringing
CMM metrology
Measure B-field over time continuously at 72 discrete locations
Measure B vs azimuth once every 3 days
Combine magnetic field with measured muon beam profile
Muon weighted B-field is 50% of uncertainty on aμ

## Slide 16
Muon-weighted magnetic field
Wire stringing
CMM metrology
Readout electronics (ASDQs)

## Slide 17
Muon-weighted magnetic field
Wire stringing
CMM metrology
Run-1 uncertainty from B-field analysis already sufficient for final dataset
Run 2/3 contains ~10x as many trolley runs as Run1
Rich dataset  a lot of interesting information about the magnetic field

## Slide 18
Summary
Wire stringing
CMM metrology
The straw tracking detectors have been crucial to the success of the g-2 experiment
Very active g-2 community in the UK, with major contributions in multiple analysis areas
Current work to improve tracking efficiency will be invaluable to the g-2 and EDM analyses
Huge datasets left to analyze with much scope for new ideas and collaboration